## Slide 1: Instructions for use
This resource is not a teaching and learning program. It should be used in conjunction with The Park and ride unit.
Classroom teachers are encouraged to add and adapt slides as required to meet the needs of their students.
Save a copy of the file to make changes to the slide deck. Go to File > Download a Copy (this downloads a copy to the computer to edit in the PowerPoint app).
To convert the PowerPoint to Google Slides:
  Upload the file into Google Drive and open it.
  Go to File > Save as Google Slides.
  (Note – conversion may cause formatting changes in the slides.)

## Slide 2: Park&Ride
Technology 7–8
Digital communications technologies and Engineering technologies and systems
20-week program of learning

## Slide 3: Weeks 1–2

## Slide 4: Learning intentions and success criteria (1)
We are learning to
understand challenges people face when finding parking and using public transport
apply an engineering design process with a focus on defining problems.
We can
explain how parking and public transport solutions can help support sustainability
clearly define a problem by considering who is affected, what the problem is, and why it matters.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 5: What should commuting look like in the future?
https://transportnsw.info/travel-info/ways-to-get-around © Transport for New South Wales

## Slide 6: Instead of this

## Slide 7: or this

## Slide 8: You have to navigate a complex road network

## Slide 9: With lots of other cars

## Slide 10: on busy roads

## Slide 11: And then where do you find a parking space ?

## Slide 12: How can we design a better parking system to improve the experience of using public transport?
Wollongong Commuter Car Park © Transport for New South Wales

## Slide 13: Define
Who is affected? | What is the problem? | Why is it important to solve?
Use these questions to clearly identify and understand the problem or challenge that needs a solution.

## Slide 14: Learning intentions and success criteria (2)
We are learning to
understand how Park&Ride works with public transport
map the steps people take when using Park&Ride.
We can
explain what a user journey is
create a visual map of the Park&Ride user journey
identify important points that affect the user’s experience.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 15: Park for free when you ride public transport
Park for free when you ride public transport (1:43)

## Slide 16: User journey
What does a user have to do to use Park&Ride?
Write the steps required:
1.
2.
3.
4.
…

## Slide 17: Creating a user journey map (example template) (1)
https://www.canva.com/design/DAG1lGNtfOs/7xkZEqg-0ZtE8QdQ8um7cw/edit
Notes: https://www.canva.com/online-whiteboard/customer-journey-map/
Creating a customer journey map using Canva template
https://www.canva.com/design/DAG1lPiMVaQ/LkhgRdHL0hdIBD91_G2VQA/edit

## Slide 18: Learning intentions and success criteria (3)
We are learning to
explore how engineered systems address societal needs and support sustainability.
We can
explain the purpose of engineered systems in society.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 19: Setting the scene – folding boom gate
Think pair share
Think about
        Where have you seen boom gates used?
        Why were they used?
        What engineered systems are like boom gates?
Share your thoughts with the person next to you
Group discussion
Document the discussion in your workbook
"Superfluous Boom Gates" by mikecogh is licensed under CC BY-SA 2.0.

## Slide 20: Public transport and sustainability
Jigsaw activity
Watch Sustainable transport development in Asia and the Pacific.
In your allocated group, respond to one of the sets of questions in the table, prior to presenting to the class.
As you listen to other groups present their responses make notes in the relevant section in the table.

## Slide 21: Learning intentions and success criteria (4)
We are learning to
connect a microcontroller to a computer and set up the programming environment
write and upload basic code to control LEDs on the microcontroller.
We can
correctly connect the microcontroller to a computer and open the programming software
write, upload, and test simple code to make an LED flash.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 22: Setting up a workspace
Create one folder (also called a directory) to save your programs into. Give it the name basics as we will use it to store example programs that show how to code for individual components.
In the screenshot on the right, there are two folders:
basics
park-and-ride
When we have learned these basics, we can create more complex programs and store those in the park-and-ride project folder.

## Slide 23: 2 options to connect a Raspberry Pi Pico

## Slide 24: Using Thonny
In addition to the menu bar, these are the four main areas we require to program in Thonny:
Toolbar (shortcut buttons to most common commands)
Code editor (the panel where users write and edit their Python code)
Shell (interactive panel provides access to the Python interpreter)
Files (not active by default and is selected under the view menu)
Notes: Teacher note: other programming tools can be used to create the code for this project. Thonny was chosen to create the screenshots for this PowerPoint but other tools like VS Code, Mu and IDLE could also be used depending on school context. For most of the Thonny screenshots the shell panel was selected under the view menu. The files panel is enabled to illustrate the two main places where the Python project files (programs) are stored.

## Slide 25: Type this code into Thonny – blink.py

## Slide 26: Starting to use Thonny
type this code in the code editor panel
use tabs on lines 7–10
lines 3 and 5 do not have to be blank
Thonny colour codes keywords like import and while True:
the asterisk next to <untitled> * indicates unsaved changes
click save

## Slide 27: Running our first script – blink.py
it is good practice to save first (but this code will run without saving)
note the asterisk <untitled> *
click green button
note the prompt changes in the shell window %Run –c $EDITOR_CONTENT
LED on the pico flashes on and off
what happens if you increase the value of x in sleep(x) ?

## Slide 28: Running blink.py
Onboard LED flashes

## Slide 29: Stopping a script
click red stop button
note the prompt changes in the shell window
KeyboardInterrupt:
LED on the pico stops flashing
click red stop button (again) to clear this

## Slide 30: Explaining blink.py
Line 1 imports the Pin class from the machine module.
The machine module provides low-level control over hardware components of a microcontroller.
The Pin class gives you the ability to configure and interact with the microcontroller’s GPIO pins.
Line 2 imports only the sleep function from the time module, rather than importing the whole module.
The time module provides various time-related functions. The sleep function pauses the execution of the program for the specified number of seconds.

## Slide 31: Explaining blink.py (continued)
Line 4 defines an object called led
‘LED’ refers to the on-board LED
Line 6 starts the while loop (lines 7–10 repeat until the program is stopped)
        sets led value to ‘on’
        sleep for 0.5 second
        sets led value to ‘off’
        sleep for 0.5 second

## Slide 32: Saving blink.py
save to This computer before uploading to the pico
(a good practice to keep a reference copy in case multiple people use the same pico)
the program will still run from either the computer or the Pico
Notes: This slide has an animation to represent a two-step process for saving a file. Click on image (or right arrow) to see second image.

## Slide 33: Checking blink.py
click run to make sure it still works
then click stop.

## Slide 34: Modifying blink.py
delete lines 7–10
replace with:
led.toggle()
sleep(1)
do not forget the TABS
click save
run the script to check it performs the same way
what is different?

## Slide 35: Uploading blink.py to the Pico
simple scripts like this can run from the computer
right click on blink.py and select Upload to /
blink.py will then show under This computer and under Raspberry Pi Pico
scripts which import external, custom modules will need the modules uploaded to the Pico to run them

## Slide 36: Where is the script running from?
Computer
Raspberry Pi Pico

## Slide 37: Make 2 LEDs blink? (optional)
Create the circuit as shown using a 330 ohm resistor and a LED and two jumper wires.
Add line 5
second_led = Pin(15, Pin.OUT)
Add line 9
second_led.toggle()
Save as blink_2leds.py
And click run.

## Slide 38: Built-in MicroPython modules
MicroPython uses the root path (”) and its “lib” subpath (‘/lib’) as default folders where modules are to be stored.
note that these paths refer to RPI Pico memory, so you must store them on the board.
the only exception is with built-in libraries, that are already available without explicit files
listed with command: help('modules')

## Slide 39: Weeks 3–4

## Slide 40: Learning intentions and success criteria (5)
We are learning to
explain the function and components of boom gates within parking stations
distinguish between DC motors and positional servos.
We can
explain what a boom gate is and why it is used in parking stations
list the good and bad things about using DC motors and servos in boom gates.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 41: List the components of this boom gate system

## Slide 42: A Beginner's Guide to Choosing & Using Motors, Servos and More
A Beginner's Guide to Choosing & Using Motors, Servos and More (18:16)
Notes: Focus on servos and DC motors. Other actuators may be useful extension if time permits.
0:00 Intro
0:54 What is an Actuator?
1:29 Linear Actuators
5:56 Servos
11:14 DC motors
13:04 Stepper Motors

## Slide 43: Learning intentions and success criteria (6)
We are learning to
correctly connect a servo motor to a microcontroller
control a positional servo motor using code and PWM signals.
We can
correctly connect a servo motor to the microcontroller
write or modify code to move a servo motor to specific angles.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 44: Servos
There are 2 main types of micro servos.
This is an image of a positional servo.
A positional servo motor is a special type of motor that can move to a specific angle or position, like turning 90 degrees.
The other type, rotational servos, can be programmed to control both the direction it spins (forwards or backwards) and how fast it spins.
The two black plastic arms with holes (above and right of the servo) are called servo horns.
Notes: If your servo has a feedback capability it will have a fourth wire lead

## Slide 45: Servo leads
Most positional micro servos have three leads
Brown, red and orange
brown – ground
red – power
orange* – signal (PWM) (* or yellow)
Black, red and white
black – ground
red – power
white – signal (PWM)
Notes: If your servo has a feedback capability it will have a fourth wire lead

## Slide 46: PWM signal lead
Depending on the manufacturer the orange (PWM signal) lead may sometimes be yellow

## Slide 47: Connect the servo as shown
Using VBUS pin to power the servo requires the Pico to be powered by the USB port

## Slide 48: Connect the servo as shown
Using VBUS pin to power the servo requires the Pico to be powered by the USB port
Notes: If your servo has a feedback capability it will have a fourth wire lead

## Slide 49: Type this code – servo_basic.py

## Slide 50: Explaining servo_basic.py
This code is a basic example to control a micro servo.
Line 1 imports Pin and PWM classes from the machine module.
Line 2 imports only the sleep function from the time module.
Line 4 defines a PWM object called sg92 assigned to pin 18, set as output.
Line 5 sets the PWM frequency to 50 Hz (this is standard for this type of servo)
Lines 7,8,10, and 11 are comments showing how the duty cycles are calculated.
Notes: Import statements:
Pin and PWM from machine: for controlling hardware pins and generating PWM signals.
sleep from utime: is used to create delays.
Duty Cycle Calculations:
Comments explain how to calculate the duty cycles for servo positions:
0.5 ms pulse (minimum position) → Duty cycle 2.5% → duty_u16(1638)
2.4 ms pulse (maximum position) → Duty cycle 12% → duty_u16(7864)
These values are for a 16-bit PWM (range 0–65535).
The pulse values (0.5 and 2.4 ms) are typical for this type of servo. Different brands or models of servos may work with these values
but if the servo seems to strain at either end position these values could be changed slightly (for example to 0.6 or 2.3)
Similarly, if a servo is not sweeping to its fullest extent (0 to 180 degrees) these values could be slightly increased.

## Slide 51: Explaining servo_basic.py (continued)
Line 13 starts the while loop (lines 14–17 repeat until the program is stopped)
Line 14 moves the servo to the minimum position duty_u16(1638)
Line 15 waits 1 second.
Line 16 moves the servo to the maximum position duty_u16(7864)
Line 17 waits 1 second.
Notes: Summary:
The code makes a servo motor sweep between two positions every second.
If you connect a servo to pin 18, it will move from one extreme to the other and back, pausing for 1 second at each end.

## Slide 52: Running servo_basic.py (1)
00:06:27
Notes: Click image to play short video.

## Slide 53: Running servo_basic.py (2)
00:09:53
Design considerations
The single arm horn has been replaced by a cross servo horn. The two larger arms will be trialled for dual attachment points, providing more stability and control for larger surfaces.
The servo has been placed into a metal frame to raise it higher (when it is back in an upright position.
Start considering how high you want the boom gate arm to operate at.
Notes: Click image to play short video.

## Slide 54: Is there a built-in servo library?
Currently the default UF2 image of MicroPython for Raspberry Pi Pico has no built-in servo library.
* Custom images like Kookaberry have additional libraries installed as their default.

## Slide 55: Options for servo library?
Thonny has a tool Manage packages that can download and install MicroPython packages (libraries). Currently it does not work on department managed devices.
Three work arounds:
use code which manually sets servo angles (see simple_servo.py example)
download and manually upload servo libraries on Pico (similar process to how PiicoDev libraries are used)
use Manage packages on a Pico connected to BYOD device (installed libraries can be used with Pico on BYOD or managed devices)
Notes: This slide uses animation. Click on image (or right arrow) to see second image.

## Slide 56: BYOD options for servo library?
Manage packages should typically work on BYOD devices. Follow steps in images on right (click to progress through steps)

## Slide 57: Where are modules and packages installed to
After Manage packages has been successfully used, a lib folder is created on the Raspberry pi Pico. “Installed” libraries are stored in this folder.
This image shows a servo folder within the lib folder. The micropython-servo package is stored in there.
To use it, use the code:
Import Servo (the entire module)
or
Import servo from Servo

## Slide 58: Type this code – servo_3steps.py

## Slide 59: Explaining servo-3steps.py (1)
This code controls a servo motor using an external servo library.
Line 1 imports only the sleep function from the time module.
Line 2 imports Servo class from the servo module.
Lines 4 and 5 are comments
Line 6 defines an object called my_Servo (based on Servo class) and assigned to pin 18.
Notes: Imports:
sleep from time: sleep method is used to create delays specified (in this script) by seconds.
Servo from servo: an external library (external to this program) used to simplify servo control.
The external library typically has a custom class by the same name. Within servo.py (
On line 6: Pin 18 is assigned to be the pin that sends PWM signal to the servo.

## Slide 60: Explaining servo-3steps.py (2)
Line 8 starts the while loop (lines 9–16 repeat until the program is stopped)
Line 9 moves the servo to the minimum position (0)
Line 10 waits 2 seconds.
Line 12 moves the servo to the middle position (90)
Line 13 waits 2 seconds.
Line 15 moves the servo to the maximum position (180)
Line 16 waits 2 seconds.
Notes: Imports:
sleep from time: sleep method is used to create delays specified (in this script) by seconds.
Servo from servo: an external library (external to this program) used to simplify servo control.
The external library typically has a custom class by the same name. Within servo.py (
On line 6: Pin 18 is assigned to be the pin that sends PWM signal to the servo.

## Slide 61: Running servo_3steps.py
This program moves the servo (and attached horn) between 3 positions.
00:12:30

## Slide 62: Learning intentions and success criteria (7)
We are learning to
describe the three orders of levers and their mechanical functions
explain significance of the woomera as a lever innovation
We can
explain when to use different levers
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 63: Force, motion and energy
Read the information in your workbook or watch Newton's 3 Laws, with a bicycle (3:32)
Describe force, motion and energy, giving examples for each

## Slide 64: Levers
Watch Simple machines: levers (2:43)
Define first, second and third order levers

## Slide 65: Woomera – Aboriginal application of the lever (1)
The Woomera is a sophisticated Aboriginal engineering innovation that uses an understanding of force and motion as applied through a lever to help launch spears further and with greater force. It is typically a long, flat piece of wood. It has a shape like a large stick or paddle.
After reading the passage in your workbook:
explain why a woomera increases throwing force

## Slide 66: Woomera – Aboriginal application of the lever (2)
Practical activity
On the school oval or similar open measure and evaluate the distance of hand thrown tennis balls and tennis balls thrown using a ball launcher.
Which method results in the longest distance?
Explain why.
"Before the Throw with ball launcher for dog" by Kate Ter Haar is licensed under CC BY 2.0.

## Slide 67: Learning intentions and success criteria (8)
We are learning to
build a working model of a boom gate using a servo motor
write (or modify) code to control a servo.
We can
assemble a boom gate model with a servo and barrier arm correctly attached
write (or modify) code to move a servo between open and closed positions.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 68: What aspects of this boom gate system can we model?

## Slide 69: Model of boom gate arm (1)
00:12:50
Notes: Click image to play short video.

## Slide 70: Model of boom gate arm (2)

## Slide 71: Model of boom gate arm (3)

## Slide 72: Simple script to model boom gate movement
Let’s save a modified version of servo_3steps.py

## Slide 73: Explaining servo_boomgate.py
This Python script controls a servo motor to alternately move a boom arm (attached to the servo horn) between a closed and open position.
Line 1 imports only the sleep function from the time module, rather than importing the whole module.
The time module provides various time-related functions. The sleep function pauses the execution of the program for the specified number of seconds.

## Slide 74: Explaining servo_boomgate.py (continued)
Line 6 creates a Servo object called my_servo. pin_id=18 specifies the GPIO pin number 18.
Line 8 starts the main loop (while loop)
Line 9 my_servo.write(90) moves the servo to a position corresponding to 90 degrees
Line 10 waits for 5 seconds with boom gate “open”.
Line 12 my_servo.write(180) moves the servo to a position corresponding to 180 degrees
Line 13 waits for 5 seconds with boom gate “closed”.

## Slide 75: Running servo_boomgate.py
Basic boom gate function
00:12:50

## Slide 76: Weeks 5–6

## Slide 77: Learning intentions and success criteria (9)
We are learning to
understand the role of sensors in automated systems such as boom gates
evaluate different sensor types for suitability in a boom gate prototype
design a sensor-based system to control a boom gate safely and reliably.
We can
explain how sensors detect vehicles and control boom gate actions
compare advantages and disadvantages of various sensor types
propose appropriate sensors and design considerations for a boom gate prototype.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 78: Ultrasonic sensor
These sensors use sound waves above human hearing range
Emit ultrasonic pulses and measure time for echo to return. Calculate distance to objects based on echo time
Used for object detection, distance measurement, and obstacle avoidance
Common in robotics, cars (parking sensors), and industrial automation
Work well in dark or dusty environments where light sensors struggle. Provide accurate and reliable non-contact measurements.

## Slide 79: Infrared sensor ‘A’ (1)
Infrared Line/Object Presence sensors detect lines, edges, and nearby objects
Emit infrared light and measure how much is reflected back
Identify contrast between surfaces (like black and white lines) or presence of objects
Used in robotics for line-following and object detection
Help machines know where to move or when an object is present. Work best with high-contrast surfaces or reflective objects.

## Slide 80: Infrared sensor ‘B’
Infrared proximity sensors detect nearby objects without touching them
Emit infrared light and measure the reflection from objects
Calculate distance based on the amount of reflected IR light
Used for object detection, obstacle avoidance, and touchless control
Common in smartphones, automatic faucets, and robotics
Work best with objects that reflect infrared light well
Provide quick and reliable sensing in close range

## Slide 81: Distance sensor (time of flight – ToF)
ToF sensors measure distance by timing how long light takes to bounce back
Emit a light pulse (usually infrared) and detect its reflection
Calculate distance based on the time taken for the light to return
Provide precise and fast distance measurements
Used in smartphones, drones, and robotics for object detection
Work well in various lighting conditions, including darkness

## Slide 82: Ambient light sensor
Ambient light sensors detect the brightness of surrounding light
Measure natural and artificial light levels
Help devices adjust screen brightness automatically
Save energy and reduce eye strain by adapting to light conditions
Commonly used in smartphones, laptops, and cameras
Provide data for smart lighting and display systems

## Slide 83: Magnetometer sensor
Magnetometers measure magnetic fields around them
Detect strength and direction of magnetic forces
Often used to find direction like a digital compass
Can sense Earth’s magnetic field for navigation
Used in smartphones, drones, and metal detectors
Help in detecting magnetic materials and changes in magnetic environment

## Slide 84: RFID sensor
This component can detect when a RFID chip is put within range of it.
RFID stands for Radio Frequency Identification
Uses radio waves to read and capture info stored on a tag
Consists of a reader (module) and a small RFID tag or card
Tags can be passive (no battery) or active (battery-powered)
Reads tags from a short to medium distance without direct contact
Commonly used for access control, inventory tracking, and identification

## Slide 85: Comparing sensor technology
Sensor type | Detection | Range / distance | Accuracy | Relative cost | Possible application
Infrared |  |  |  |  | 
Ultrasonic |  |  |  |  | 
Magnetometer |  |  |  |  | 
RFID |  |  |  |  | 
Time of flight |  |  |  |  | 
Induction loops |  |  |  |  | 
Notes: Teacher notes:
This link has advantages and disadvantages for most of the commonly used sensors - https://au.element14.com/smart-parking-solutions-the-iot-sensors-space-race

## Slide 86: Plotting sensor technology cost versus accuracy
Low accuracy
Low total cost
High total cost
High accuracy
Notes: Teacher notes:
This link has advantages and disadvantages for most of the commonly used sensors - https://au.element14.com/smart-parking-solutions-the-iot-sensors-space-race

## Slide 87: Parking bay sensors
How might these sensors work?

## Slide 88: Learning intentions and success criteria (10)
We are learning to
connect an infrared (IR) sensor to a microcontroller
write code to read the IR sensor values and use it to control servo movement.
We can
correctly connect an IR sensor to the microcontroller
write or modify code to read sensor signals.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 89: Infrared sensor ‘A’ (2)

## Slide 90: Type this code into Thonny – infrared_sensorA.py

## Slide 91: Explaining infrared_sensorA.py
This program uses an infrared (IR) line sensor to detect the presence of an object (like a car), lights an LED as a signal, and moves a servo motor to open or close the boom gate.
Line 1 imports the Pin class from the machine module.
The machine module provides low-level control over hardware components of a microcontroller.
The Pin class provides the ability to configure and interact with the microcontroller’s GPIO pins.

## Slide 92: Explaining infrared_sensorA.py (continued)
Line 2 imports only the sleep function from the time module, rather than importing the whole module.
The time module provides various time-related functions. The sleep function pauses the execution of the program for the specified number of seconds.
Notes: By importing sleep directly, you can call it as sleep(seconds) instead of time.sleep(seconds), which can make the code cleaner and slightly more concise.

## Slide 93: Running infrared_sensorA.py

## Slide 94: Learning intentions and success criteria (11)
We are learning to
enhance a working prototype of a boom gate with automated control
use sensors to detect approaching objects and control servo movements.
We can
use conditional logic to open or close the boom gate automatically
write or modify code to automate the boom gate using sensor readings
use sensor readings to control a servo motor.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 95: Recap
Last lesson we got the IR sensor to detect objects in front of it

## Slide 96: Goal automate the servo with input from the sensor.

## Slide 97: Explaining infrared_sensorA_servo.py
Pin (from machine) used to control and monitor GPIO pins.
sleep (from time) pauses code execution for a specified duration.
Servo (from servo) handles control of a servo motor.
Controls an LED connected to GPIO pin 25 (set as an output).

## Slide 98: Explaining infrared_sensorA_servo.py (continued)
Reads the state of an IR sensor connected to GPIO pin 20 (set as an input).
Controls a servo motor connected to GPIO pin 18 using PWM.
Each iteration checks the IR sensor’s current value:
IR_sensor.value() == 0: This typically means an object has been detected (the IR sensor output goes LOW when blocked).

## Slide 99: Upload infrared_sensorA.py
Now the servo library is loaded onto the Pico this script can be run from either the computer or the Pico
but if we want to untether the Pico from the computer, we need to place the program on the Pico
right click on infrared_sensorA.py
select Upload to /

## Slide 100: Running infrared_sensorA_servor.py
00:09:34
Notes: Click image to play short video.

## Slide 101: What does that error mean?
As each Pico gets assigned a unique COM port on each computer it is connected to, this error could also mean the Pico assigned COM3 is not connected (or a different Pico is plugged in).
Typically, this error means Thonny cannot sense if the Pico it last communicated with is plugged in.

## Slide 102: Learning intentions and success criteria (12)
We are learning to
identify and test an alternative sensor type to control a servo-driven boom gate
write or adapt code to automate the boom gate using a new sensor.
We can
explain how the new sensor works and how it differs from the infrared sensor
write or adapt code to read the sensor data and control a servo.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 103: Same same but different
3 infrared sensors that operate differently
Sensor | Voltage requirement | Range | Cost
‘Duinotech’ LM393 (left) | 3.3-5V | 10mm | ~$1.20
Unknown (middle) | 3–5V | 20–300mm | ~$4.60
‘KeyesIR’ (right) 4 pins Arduino compatible | 3.3–5V | 20–400mm | ~$3.40
Notes: Three different infrared sensors that all work on the same principle of emitting IR light and detecting what IR light is received (reflected) back. They operate differently in how they process the input received on the receiving diode.

## Slide 104: Save as
infrared_sensorA.py  infrared_sensorB.py
To save time, select infrared_sensorA.py and save a copy of as:
infrared_sensorB.py
In the next step we modify some values.
(dependant on which sensor is being used)
Notes: This slide has animation applied to the images. It represents the sequence of steps in saving a Micropython script (infrared_sensorA.py  infrared_sensorB.py)

## Slide 105: One change (if using this sensor)
Change Pin number on line 5 from:
IR_Sensor = Pin(20, Pin.IN)
to
IR_Sensor = Pin(22, Pin.IN)

## Slide 106: Connecting infrared sensor B
IR_Sensor = Pin(22, Pin.IN)
Before running this new program we also need to make sure we plug the new sensor into Pin 22 socket.

## Slide 107: Explaining infrared_sensorB.py
This program uses an infrared (IR) sensor to detect the presence of an object (like a car), lights an LED as a signal, and moves a servo motor to open or close the boom gate.
Line 1 imports machine library to allow control of microcontroller pins (input/output).
Line 2 imports time module provides time-related functions like sleep

## Slide 108: Explaining infrared_sensorB.py (continued)
Line 4 sets Pin 25 (onboard LED) to output pin (used for visual feedback).
Input pin connected to an IR sensor. It detects whether something is in front of it.

## Slide 109: Overhead view of car approaching sensor and boomgate
00:07:90
Notes: Click image to play short video.

## Slide 110: Possible configuration for two sensors
The second sensor could be used to sense when the car was safely through the boom gate area.

## Slide 111: Weeks 7–8

## Slide 112: Learning intentions and success criteria (13)
We are learning to
understand what mechanical linkages are and their basic function
explore different types of linkages and how they control motion.
We can
explain the key components of a linkage (links and joints)
observe and describe how motion is transmitted through linkages.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 113: Framing the design challenge in different ways
Open-ended design focus
"How could you redesign the boom gate arm or its movement mechanism to ensure it clears the low ceiling of a parking station when fully open, while still reliably blocking vehicles when closed?“
Constraint-based problem solving
"Given that the boom gate arm must open without hitting a low ceiling in a parking station, what design changes or alternative movements could you implement to maintain safe vehicle clearance and efficient operation?“
Application and innovation
"The boom gate arm in your model opens by rotating vertically but there is a height restriction in the parking station. Propose and explain a design solution that overcomes this height limitation—such as changing the arm’s shape, movement path, or mounting position—while keeping the gate functional."

## Slide 114: Linkage systems (1)
A linkage is a system made of bars (or links) connected by pin or rotating joints that work together to create movement. Linkages help transfer motion and force from one part to another. They are used in many machines, like cranes and robotic arms.
Sketch what you think a five-bar linkage system for a folding boom gate would look like. Label the components.
Consider a multilevel car park. Outline the factors that could impact the size of each lever arm.

## Slide 115: Linkage systems (2)
Arglin Kampling, CC BY-SA 4.0 <https://creativecommons.org/licenses/by-sa/4.0>, via Wikimedia Commons
Notes: What do you notice about these different linkages?
They all produce the same path.

## Slide 116: Learning intentions and success criteria (14)
We are learning to
apply engineering processes to create and evaluate prototypes.
collect information to develop engineered solutions.
We can
produce and evaluate prototypes.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 117: Prototype production, testing and evaluation
Practical activity
Working in small groups, produce five-bar linkage prototypes using techniques Lego, Meccano, cardboard and split pins or similar.
Experiment with arm length and pin locations.
Evaluate each prototype.
Sketch your linkage that most closely represents a folding boom.
"Radial truss joint construction" by aotus is licensed under CC BY 2.0.

## Slide 118: Learning intentions and success criteria (15)
We are learning to
use graphical communication techniques to present ideas for engineered systems.
We can
apply prototyping data to produce drawings that communicate and engineered system.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 119: Folding boom gate design
Annotated ideas sketches
Using the ideas from the previous activities and your prior knowledge sketch and annotate 4 boom gate ideas.

## Slide 120: Learning intentions and success criteria (16)
We are learning to
test and evaluate prototypes for functionality.
make adjustments to improve the prototype’s performance.
We can
identify issues and make effective adjustments to improve my folding boom prototype.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 121: Folding boom gate prototype production
Practical activity
Using the materials provided and following teacher instruction
Produce a prototype of your selected design
Test for functionality
Make adjustments
Restest

## Slide 122: Weeks 9–10

## Slide 123: Learning intentions and success criteria (17)
We are learning to
develop skills in creating 3D models and orthogonal drawings according to AS1100 standards.
We can
students demonstrate basic proficiency in using CAD software
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 124: Introduction to CAD
CAD stands for Computer-Aided Design. It's a type of software that helps people create detailed drawings and models of objects, buildings, and even machines using a computer. CAD makes it easier to design and visualise ideas, allowing users to see how their creations will look and function before they are built. It's widely used in fields like architecture, engineering, and product design.

## Slide 125: CAD (1)
3D Modelling
3D modelling is the process of creating a three-dimensional representation of an object or scene using computer software. In 3D modelling, designers build a virtual version of something, which can be anything from a simple shape to a complex character or environment. These models can be viewed from different angles and manipulated just like real objects. 3D modelling is commonly used in industries like animation, video game design, architecture, and product development to visualise and present ideas before they are made in real life.

## Slide 126: CAD (2)
Orthogonal drawing
Orthogonal drawing, according to AS1100, refers to a method of representing three-dimensional objects in two dimensions using multiple views, typically the front, top, and side views.
In orthogonal drawing, each view shows only two dimensions, but when combined, they provide a complete picture of the object's shape and size. This method is essential for accurately conveying design specifications in engineering and architecture.

## Slide 127: CAD (3)
Practical activity
Complete one of the following:
An orthogonal drawing,
3D model or
component of a folding boom gate.

## Slide 128: Weeks 11–12

## Slide 129: Learning intentions and success criteria (18)
We are learning to
learning to choose and use materials, tools, and technologies to design and build an engineering product.
We can
apply knowledge of tools, materials and equipment through the production of a quality engineered product.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 130: Materials selection and justification
Jigsaw
In your allocated group, research and describe one material from the list:
Plywood
Aluminium
Fibre glass
Steel
Timber
PVC
Report your finding to the class
"holey cube in birch plywood" by jared is licensed under CC BY 2.0.

## Slide 131: Learning intentions and success criteria (19)
We are learning to
understand the requirements and processes for preparing components for manufacture using different methods such as hand production, laser cutting, and 3D printing.
We can
explain and plan how each component will be manufactured (by hand, laser cutting, or 3D printing).
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 132: Preparing for production
Practical activity
What components do we need to make?
What materials will they be made from?
How will they be made?
What do we need to set up for manufacture.

## Slide 133: Weeks 13–14

## Slide 134: Learning intentions and success criteria (20)
We are learning to
apply different manufacturing methods for producing components,
safely use hand tools and machines and apply these techniques to construct a folding boom gate.
We can
progressively use tools and equipment with increasing independence.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 135: Component manufacture and assembly
Practical activity
Components can be manufactured in a variety of ways, including using hand tools and equipment, laser cutting and 3D printing.
Experiment with tools, equipment and techniques throughout the manufacturing process.

## Slide 136: Learning intentions and success criteria (21)
We are learning to
use design factors to check how good an engineered solution is.
We can
evaluate engineered solutions against a criteria.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 137: Testing and evaluation
Using the table in your workbook rate and comment on your manufactured design in terms of:
Functionality
Design completeness
Structural integrity
Ease of operation
Aesthetic appeal
Materials used
Innovation and creativity
Accuracy of movement
Efficiency

## Slide 138: Learning intentions and success criteria (22)
We are learning to
understand how automation improves parking stations
understand the technology used to automate parking stations.
We can
explain how parking guidance systems help drivers find available spaces
describe how sensor data is used to update parking information.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 139: Commuter carpark

## Slide 140: Weeks 15–16

## Slide 141: Learning intentions and success criteria (23)
We are learning to
display text and numbers on the OLED screen
integrate sensor data to show real-time information on the OLED screen.
We can
correctly connect an OLED screen to a microcontroller
write or modify code to display specific text or numbers on the OLED screen
update the OLED display in real time.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 142: Sample

## Slide 143: Upload PiicoDev_SSD1306.py
PiicoDev_SSD1306.py is a Python library that makes it easy to program and control PiicoDev brand SSD1306 OLED screens.
It provides functions and classes to control SSD1306 OLED displays.
It acts as a driver, allowing you to easily display text, graphics, and other information on the screen from your microcontroller.

## Slide 144: Upload PiicoDev_Unified.py
PiicoDev_Unified.py acts as a unified driver library that makes coding with multiple PiicoDev devices simpler and more consistent.

## Slide 145: Type this code – OLED.py

## Slide 146: OLED module wiring
PiicoDev OLED module can be connected to breadboards with either jumper leads or an adapter

## Slide 147: OLED module
The PiicoDev OLED module is connected via the expansion board

## Slide 148: Saving OLED.py
save to This computer before uploading to the pico
the program will still run from either the computer or pico.
Notes: This slide has animations applied to the images to show a multi-step process of saving a file. Click on the image to follow the process.

## Slide 149: Explaining OLED.py
This code is for drawing words and numbers on an OLED display
Line 1 imports all the necessary functions and classes to control the display.
Line 2 initialises the display object, preparing it for drawing.
Line 3 text string “Car spaces left” assigned to variable myString
Line 4 integer value ‘4’ assigned to variable myNumber
Notes: Explanation (student level):
This code is for drawing words and numbers on a small screen (an OLED display).
from PiicoDev_SSD1306 import *: Brings in the tools needed to work with the display.
display = create_PiicoDev_SSD1306(): Gets the display ready to use.
myString = "Car spaces left": Sets up some words to show.
myNumber = 4: Sets up a number to show.
The next lines show words and numbers at different places on the screen:
display.text("Park & Ride", 0,0, 1): Shows "Park & Ride" at the top.
display.text(myString, 0,15, 1): Shows "Car spaces left" a bit lower.
display.text(str(myNumber), 0,30, 1): Shows the number 4 even lower down.
Finally, display.show() makes everything appear on the screen.

## Slide 150: Explaining OLED.py (continued)
The display.text() method is called three times to queue text rendering at specific pixel coordinates.
Line 7 at (0, 0), the literal string "Park & Ride" is drawn.
Line 8 at (0, 15), the variable myString ("Car spaces left") is drawn.
Line 9 at (0, 30), the integer myNumber is converted to a string and drawn.
Line 10 display.show() updates the display to render all the queued text.
Notes: Explanation (student level):
This code is for drawing words and numbers on a small screen (an OLED display).
These lines show words and numbers at different places on the screen:
display.text("Park & Ride", 0,0, 1): Shows "Park & Ride" at the top.
display.text(myString, 0,15, 1): Shows "Car spaces left" a bit lower.
display.text(str(myNumber), 0,30, 1): Shows the number 4 even lower down.
Finally, display.show() makes everything appear on the screen.

## Slide 151: Running OLED.py

## Slide 152: Connected components

## Slide 153: What other forms of directions or information could be communicated in digital signage?

## Slide 154: Learning intentions and success criteria (24)
We are learning to
understand RFID technology as a sensor input device
connect an RFID reader module to a microcontroller.
We can
explain what RFID is and how it reads cards with unique IDs
scan different cards and see their unique ID numbers.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 155: Boom gates with sensors

## Slide 156: RFID swipe cards

## Slide 157: Type this code – read_card_id.py

## Slide 158: Upload PiicoDev_RFID.py
PiicoDev_RFID.py library makes it easy to communicate with and control PiicoDev brand RFID modules.
It provides ready-made functions to initialise the RFID reader, detect RFID tags, and read their unique IDs.

## Slide 159: Upload PiicoDev_RFID_Expansion.py (optional)
This is an optional addition and none of its functionality has been used in this project.
If it is not uploaded to the pico a message is printed in the shell asking if the user wants to install it.

## Slide 160: Explaining read_card_id.py
This program uses an RFID reader (in this example PiicoDev RFID module) to check for the presence of an RFID tag and, when detected, reads and prints the tag’s unique identifier.
Lines 1 to 3 import libraries:
PiicoDev_RFID allows you to communicate with the RFID reader module.
PiicoDev_Unified (sleep_ms) gives you a function to pause (sleep) the code, in milliseconds.

## Slide 161: Explaining read_card_id.py (continued)
Line 4 creates an object “rfid” that interfaces with the RFID hardware, allowing the rest of the code to access RFID-reading functions.
Line 6 prints a user prompt to shell (or console)
Line 8
Line 9 checks if an RFID tag is presented (or close enough) to the reader to be detected.
Line 10 reads the unique identifier (ID) from the detected RFID tag.

## Slide 162: Explaining read_card_id.py (continued again)
Line 11 commented out, but if uncommented this line can provide extra card details.
Line 13 displays the tag’s ID in the shell (or console)
Line 15 waits for 100 milliseconds before repeating the loop.

## Slide 163: Running read_card_id.py
Running read_card.py puts the reader into a mode of waiting for a card

## Slide 164: Running read_card_id.py (continued)

## Slide 165: Learning intentions and success criteria (25)
We are learning to
combine RFID card reading with servo control to open and close a boom gate
write code that controls a boom gate opening and closing based on authorised RFID card swipes.
We can
connect an RFID reader and servo motor to a microcontroller
integrate RFID reading with servo control to operate the boom gate.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 166: Prior knowledge
RFID tags have unique IDs
RFID devices can detect and read unique data from objects or tags.
Positioning the servo at different angles simulates opening/closing the boom gate.
Conditional logic uses if...else to perform actions based on sensor input.
Use delays to control action timing.
Real-world application: automated decisions can control physical devices for security, access control, or other purposes.

## Slide 167: Connecting RFID and servo
Servo connection uses same pins
Ground – (breadboard 18)
Power – VBUS (breadboard 1)
18 – signal – GPIO 18 (breadboard 17)
RFID connection uses
SDA (blue) – GPIO 8
SCL (yellow) – GPIO 9
Ground (black) – any available ground pin
VCC (red) – 3V3

## Slide 168: Type this code – RFID_servo.py

## Slide 169: Save RFID_servo.py
save to This computer before uploading to the pico
then upload to Raspberry Pi Pico.
Notes: This slide has animations applied to the images to show a multi-step process of saving a file. Click on the image to follow the process.

## Slide 170: Explaining RFID_servo.py
This program uses an RFID reader and a servo motor to control access through the boom gate. The boom gate will open (the servo rotates to open position) only if a scanned RFID tag matches a specific, pre-approved ID.
This code waits for an RFID tag. If the tag matches the authorised ID, it opens the boom gate for 5 seconds, then closes it. If not authorised, the gate stays closed and prints a warning.

## Slide 171: Explaining RFID_servo.py (continued)
Lines 1 to 3 import libraries:
PiicoDev_RFID allows you to communicate with the RFID reader module.
PiicoDev_Unified (sleep_ms) gives you a function to pause (sleep) the code, in milliseconds.
servo.Servo lets you control a servo motor.
Line 5 creates an object to talk to the RFID module so you can check for RFID tags and read their ID numbers.

## Slide 172: Explaining RFID_servo.py (continued again)
Lines 6 creates a servo object connected to pin 18, which controls the physical servo with a PWM signal
Line 8 displays a message telling the user to bring an RFID tag close to the reader.
Lines 10 starts the main while loop checking for RFID tags repeatedly.
Lines 11 to 13 are the same as read_card_id.py
Line 14 checks if the scanned tag matches the stored ID (is it authorised ?).

## Slide 173: Explaining RFID_servo.py (continued final)
Line 15 print to the shell “Authorised”
Line 16 the servo moves to 180° (boom gate opens)
Line 17 waits for 5 seconds (5000 milliseconds)
Line 18 the servo moves to 90° (boom gate closes)
Line 19 else: if the ID does not match
Line 20 print to the shell “Not authorised”
Line 21 waits for 100 milliseconds before repeating the check (while loop).

## Slide 174: Running RFID_servo.py
When a “valid” tag is brought near the RFID sensor this program prints “Authorised”.
We could change this code to perform a different action, like get the servo to raise the boom gate.
Similar code was used in infrared_sensorA_servo.py and infrared_sensorB_servo.py (lines 12 to 15 of these programs).
The next task could be to check against a list of “valid” tag IDs.
How could we check for a list of “valid” card IDs?

## Slide 175: Running RFID_servo.py (continued)
When an “invalid” tag is brought near the RFID sensor this program prints “Not authorised”.
Note the different card ID: 04:5A:B8:FA:12:72:81
We could change this code to perform a different action, like give directions to go to the payment machine or turn an LED on or somehow give clear signal to the user that something is wrong and what to do next.

## Slide 176: Running RFID_servo.py (video)
00:08:94
Notes: Click image to play short video.

## Slide 177: Learning intentions and success criteria (26)
We are learning to
[insert learning intention]
[insert learning intention]
We can
[classroom teacher to insert co-constructed success criteria]
[classroom teacher to insert co-constructed success criteria].
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 178: What is the difference?
Ultrasonic sensors
Besides the top sensor has a green board and the lower sensor has a blue board.
The top sensor can run on 3.3V which makes it well suited to microcontrollers like the Pico
The lower sensor requires 5V which restricts how it is used with Pico boards. However, it is well suited for microcontrollers like the Arduino

## Slide 179: Visual guides and sample code are provided for this version

## Slide 180: Connecting the ultrasonic sensor
This sensor sends out a sound wave. It waits for the sound to bounce back (echo).
The time it takes for the echo to come back is used to figure out how far away the object is.
Notes: Teacher note:
The jumper leads of the Echo and Trig pins appear crossed over in the diagram, but this is only due to the fixed orientation of the sensor within the software used to create the diagram.

## Slide 181: Type this code – ultrasonic.py

## Slide 182: Saving ultrasonic.py
save to This computer before uploading to the pico
running from either computer or pico will work
Notes: This slide has animations applied to the images to show a multi-step process of saving a file. Click on the image to follow the process.

## Slide 183: Explaining ultrasonic.py
This program uses an ultrasonic sensor to measure the distance to an object (in centimetres) and prints the result every half-second. The ultrasonic sensor works by emitting a sound pulse and timing how long it takes for the echo to return.
Line 1 import machine library used to control and read digital input/output pins on the microcontroller.
Line 2 provides time-related functions like sleep and measuring elapsed time.

## Slide 184: Explaining ultrasonic.py (1)
The code measures how far away something is using a four-pin ultrasonic sensor
The trigPin is used to send the signal.
Line 4 trigPin is set as an output pin (GPIO 16) to send a trigger pulse to the sensor.
The echoPin listens for the reflected signal.
Line 5 echoPin is set as an input pin (GPIO 17) to receive the echo signal from the sensor.
Line 7 value for speed of sound is set to 340 m/s used for distance calculations.

## Slide 185: Explaining ultrasonic.py (2)
Optical Extension
Line 10 starts defining getSonar() function:
These actions will occur when and every time the function is called.
The trigger pin is set high for 10 microseconds, telling the sensor to send out an ultrasonic pulse.
The code waits for the echo pin to go high (when the pulse is received back), marking the start time.
The code waits for the echo pin to go low (end of the echo), marking the stop time.

## Slide 186: Explaining ultrasonic.py (3)
Optical Extension
Line 20 calculates the duration of the pulse.
Line 21 distance is calculated using the formula:
distance = (duration * speed_of_sound) / 2
distance = pingTime * soundVelocity // 2 // 10000
(this line also converts result to centimetres)
Line 22 the function returns distance as an integer.

## Slide 187: Explaining ultrasonic.py (4)
Line 26 the program waits 2 seconds at start to allow the sensor to stabilise (settle).
Line 27 then it starts the main while loop
Line 28 waits half a second
Line 29 does two main actions:
Calls the with getSonar() function which measures the distance of any object in front of the sensor, and it prints this measured distance after the string ‘Distance: ’ and prints string ‘cm’ after it.

## Slide 188: Running ultrasonic.py
  Records the stop time (pingStop) when echoPin goes LOW.
  Calculates the duration (pingTime) that the echoPin stayed HIGH, which corresponds to the round-trip time for the signal.

## Slide 189: File management
Many of the files in your “basics” directory have served their purpose. Rather than delete them, we will move some of the programs (those highlighted) into a different directory.
The highlighted files are programs that have been written for a boom gate context and/or combined functions of sensors and the servo.
Do not change anything on the pico just yet.

## Slide 190: New working space
If not already done, create a new directory park-and-ride and copy the highlighted files from the previous slide into this directory.
Now you can combine code from each of these examples to further automate the boom gate and provide a digital signage for parking station users to improve their user experience.

## Slide 191: Weeks 17–18

## Slide 192: Learning intentions and success criteria (27)
We are learning to
analyse existing digital solutions for parking availability
identify user needs and evaluate how well these solutions meet them.
We can
identify key UI elements in Park&Ride webpages or apps that display parking availability
discuss strengths and weaknesses of existing solutions from a user’s perspective.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 193: Locations and availability
Are there ways to make this data more useful ?
What else would you like to know?
© Transport for NSW
https://transportnsw.info/travel-info/ways-to-get-around/drive/parking/transport-parkride-car-parks#locations_and_availability

## Slide 194: Park and Pay video
Park'nPay (0:42)

## Slide 195: Learning intentions and success criteria (28)
We are learning to
understand what a user journey is and why it is important
create a user journey to identify user needs when finding vacant car spaces via an app or webpage.
We can
define the steps a user takes when using an app to find a car space
identify different user types and their needs
create a visual user journey that shows key actions and pain points.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 196: Creating a user journey map (example template) (2)
https://www.canva.com/design/DAG1lGNtfOs/7xkZEqg-0ZtE8QdQ8um7cw/edit
Notes: https://www.canva.com/online-whiteboard/customer-journey-map/
Creating a customer journey map using Canva template
https://www.canva.com/design/DAG1lPiMVaQ/LkhgRdHL0hdIBD91_G2VQA/edit

## Slide 197: Weeks 19–20

## Slide 198: Learning intentions and success criteria (29)
We are learning to
understand what a digital prototype is and its purpose
use basic UI design principles
build simple digital prototypes of designs.
We can
explain why digital prototypes are important for testing and improving design ideas
apply key UI design principles to ensure my screen designs are clear, consistent, simple, and accessible
confidently use UI prototype software.
Notes: Notes for teachers:
Learning intentions and success criteria are best co-constructed with students. Adapt the learning intention as required and add matching success criteria.
For more information See ⁠AITSL or the NSW Department of Education explicit teaching strategies, ⁠Sharing learning intentions and ⁠Sharing success criteria
LISC is not necessarily presented at the beginning of the lesson. Teacher needs to consider most effectual time to introduce
LISC should be revisited during the lesson to support students' evaluation of their learning

## Slide 199: Screen Flow template
https://www.canva.com/design/DAG1lXjpQnc/OW5C7fChdu24LhQjoibXrQ/edit

## Slide 200: References (1)
This presentation contains NSW Curriculum and syllabus content. The NSW Curriculum is developed by the NSW Education Standards Authority. This content is prepared by NESA for and on behalf of the Crown in the right of the State of New South Wales. The material is protected by Crown copyright.
Please refer to the NESA Copyright Disclaimer for more information https://educationstandards.nsw.edu.au/wps/portal/nesa/mini-footer/copyright.
NESA holds the only official and up-to-date versions of the NSW Curriculum and syllabus documents. Please visit the NSW Education Standards Authority (NESA) website https://educationstandards.nsw.edu.au/wps/portal/nesa/home and the NSW Curriculum website https://curriculum.nsw.edu.au.
Technology 7-8 © NSW Education Standards Authority (NESA) for and on behalf of the Crown in right of the State of New South Wales, 2023.
The Engineering Mindset 13 December 2022), What is a servo motor and what does it do? (3:28), YouTube, accessed 17 September 2025.
Let’s grow up 21 April 2025, How a DC motor works in 3D – Working principle of DC motor (4:00), YouTube, accessed 17 September 2025.
Ted-Ed 20 September 2012, Newton's 3 Laws, with a bicycle (3:32), YouTube, accessed 17 September 2025.
Engineezy 7 December 2024, robotic arms, YouTube, accessed 17 September 2025.
TAJFUN PLANINA 5 November 2015, cranes, YouTube, accessed 17 September 2025
Mia Wang 7 June 2025, Folding barrier gate (0:25), YouTube, accessed 17 September 2025

## Slide 201: References (2)
MooMooMath and Science 27 May 2020, Simple machines:levers (2:43), YouTube, accessed 17 September 2025
Technology 7-8 © NSW Education Standards Authority (NESA) for and on behalf of the Crown in right of the State of New South Wales, 2023.
https://sydney.org.au/wp-content/uploads/2022/08/Committee-for-Sydney-Better-Parking-for-Better-Places-August-2022.pdf
https://www.mynrma.com.au/-/media/nrmaheadless/files/smarter-parking.pdf
https://www.transport.nsw.gov.au/sites/default/files/media/documents/2017/sustainable-design-guidelines-v4.pdf

## Slide 202: Copyright
© State of New South Wales (Department of Education), 2025
The copyright material published in this resource is subject to the Copyright Act 1968 (Cth) and is owned by the NSW Department of Education or, where indicated, by a party other than the NSW Department of Education (third-party material).
Copyright material available in this resource and owned by the NSW Department of Education is licensed under a Creative Commons Attribution 4.0 International (CC BY 4.0) license.
This license allows you to share and adapt the material for any purpose, even commercially.
Attribution should be given to © State of New South Wales (Department of Education), 2025.
Material in this resource not available under a Creative Commons license:
the NSW Department of Education logo, other logos and trademark-protected material
Material owned by a third party that has been reproduced with permission. You will need to obtain permission from the third party to reuse its material.
Links to third-party material and websites
Please note that the provided (reading/viewing material/list/links/texts) are a suggestion only and implies no endorsement, by the New South Wales Department of Education, of any author, publisher, or book title. School principals and teachers are best placed to assess the suitability of resources that would complement the curriculum and reflect the needs and interests of their students.
If you use the links provided in this document to access a third-party’s website, you acknowledge that the terms of use, including licence terms set out on the third-party’s website apply to the use which may be made of the materials on that third-party website or where permitted by the Copyright Act 1968 (Cth). The department accepts no responsibility for content on third-party websites.